SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 1
    

    
    
                      SAIA - P8 REDUCED PROTOCOL DESCRIPTION
                     +======================================+
    
    
    
    
                      REVISION HISTORY        DD-EPFW6-024
                     +------------------------------------+
    
                      23/11/93  GK  Creation based on full description
                      3/1/93    GK  Corrected layout of document
    
    
    1. INTRODUCTION
       ------------

    1.1. Purpose
         -------

    The purpose of this document is the specification of the datagrams and
    functions used in the SAIA-P8  protocol and its relation to the
    transmission protocols.
    
    1.2. Scope
         -----

    The SAIA-P8  Protocol allows the exchange of medias and the program
    control between different PCD stations and between PCD station and
    Programming Units and/or Process Management Systems.  The SAIA-P8
    Protocol may be used over any byte transparent connection (asynchronous
    connections or OSI Transport Protocols).
    
    The scope of the document is the definition of the syntax and procedures
    of the application, presentation and session layer protocols.

    SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 2
    

    TABLE OF CONTENTS
    =================


    


    1. INTRODUCTION ......................................................1
    1.1. Purpose .........................................................1
    1.2. Scope ...........................................................1
    1.3. Definitions and Abbreviations ...................................3
    1.4. References ......................................................3

    2. GENERAL DESCRIPTION ...............................................4

    3. APPLICATION LAYER .................................................4
    3.1. Modelling the provided Service ..................................4
    3.2. Formats of the Medias ...........................................4
    3.2.1. Binary Format .................................................4
    3.2.2. Integer Format ................................................4
    3.2.3. Floating-Point Format .........................................5
    3.3. Application Service .............................................6
    3.3.1. Variable Access Service .......................................6
    3.3.2. Status Service ................................................6
    3.4. Application Protocol ............................................7
    3.5. Conformance Classes .............................................7

    4. PRESENTATION LAYER ................................................8
    4.1. Syntax Representation ...........................................8
    4.2. General Definitions .............................................8
    4.3. Reduced Protocol Telegrams ......................................10
    4.3.1. Read Telegrams ................................................10
    4.3.2. Write Telegrams ...............................................10
    4.3.3. Read Status Telegram ..........................................10
    4.4. FURTHER TELEGRAMS ...............................................11
    4.4.1.  Read data block ..............................................12
    4.4.2.  Write data block .............................................12
    4.4.3.  Read block addresses .........................................12
    4.4.4.  Read block sizes .............................................12

    5. SESSION LAYER .....................................................13
    5.1. Session Layer Service ...........................................13
    5.2. Session Layer Protocol ..........................................13
    5.2.1. Description of the used control-characters ....................13
    5.2.2. Message transmission ..........................................15
    5.2.3. Invocation of response messages ...............................16
    5.2.4. Simplex and Half-Duplex Protocol ..............................16
    5.3. Conformance Classes .............................................17

    6. TRANSMISSION PROTOCOLS ............................................18
    6.1. Point to Point connection .......................................18

    SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 3
    

    1.3. Definitions and Abbreviations
         -----------------------------

    PCD      Programmable Controller generation D of SAIA
    OSI      Open System Interface
    media    flags,registers,timers,counters,inputs, outputs, real-time
             clock, PCD status or display register of a SAIA-PCD
    
    1.4. References
         ----------

    DD-EPFW6-008    The Full P8 protocol description 18/11/93
    

    SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 4
    

    2. GENERAL DESCRIPTION
       -------------------

    3. APPLICATION LAYER
       -----------------

    3.1. Modelling the provided Service
         ------------------------------

    This specification makes use of the terms Client and Server in order to
    describe the model of the provided Service by the SAIA-P8 Protocol for the
    PCD family.  The Server is defined as the system that behaves externally
    as a PCD for a particular service request. The Client is the system that
    makes use of the PCD for some particular purpose via a service request.
    The Client may be another PCD or any other system which can drive the
    protocol (adapted from ISO 9506/1).
    
    SAIA-PCD or other computer            SAIA-PCD
    ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
    ³ Client (active)   ³             ³ Server (passive)                   ³
    ³   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´             ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³
    ³   ³ Requesting    ³             ³ Responding    ³   ³ the medias   ³ ³
    ³   ³   ÚÄÄÄÄÄÄÄÄÄÄÄ´  Request    ÃÄÄÄÄÄÄÄÄÄÄÄ¿   ³   ³ and programs ³ ³
    ³   ³   ³ Sending   ÃÄÄÄÄÄÄÄÄÄÄ>ÄÄ´ Receiving ÃÄÄÄÅÄÄ>³ of the       ³ ³
    ³   ³   ÀÄÄÄÄÄÄÄÄÄÄÄ´             ÃÄÄÄÄÄÄÄÄÄÄÄÙ   ³   ³ SAIA PCD     ³ ³
    ³   ³   ÚÄÄÄÄÄÄÄÄÄÄÄ´  Response   ÃÄÄÄÄÄÄÄÄÄÄÄ¿   ³   ³              ³ ³
    ³   ³   ³ Receiving ÃÄ<ÄÄÄÄÄÄÄÄÄÄÄ´ Sending   ³<ÄÄÅÄÄÄ´              ³ ³
    ³   ³   ÀÄÄÄÄÄÄÄÄÄÄÄ´             ÃÄÄÄÄÄÄÄÄÄÄÄÙ   ³   ³              ³ ³
    ³   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´             ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ             ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
    
    3.2. Formats of the Medias
         ---------------------

    3.2.1. Binary Format
           -------------

    Binary values are represented by one Bit 0 or 1. For the transmission they
    may be coded as the ASCII characters '0' and '1'.
    
    3.2.2. Integer Format
           --------------

    The integer format is based on 32 Bits with the following format:
    
          ³               ³               ³               ³               ³
          ÚÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄ¿
          ³s³x³x³x³x³x³x³x³x³x³x³x³x³x³x³x³x³x³x³x³x³x³x³x³x³x³x³x³x³x³x³x³
          ÀÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÙ
          31                                                             0
          where     x - 31 bit value
                    s - sign
    
    The sign bit is a zero for a positive value, and a one for a negative
    value.

    SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 5
    

    The range allowed by this format is as follows:
    
    DECIMAL
            2'147'483'647       >   VALUE    >  -2'147'483'648
    
    BINARY (HEXADECIMAL)
    
           7FFF'FFFF            >   VALUE    >   8000'0000
    
    3.2.3. Floating-Point Format
           ---------------------

    The floating point format is based on 32 Bits with the following format:
    
          ³               ³               ³               ³               ³
          ÚÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄ¿
          ³m³m³m³m³m³m³m³m³m³m³m³m³m³m³m³m³m³m³m³m³m³m³m³m³s³e³e³e³e³e³e³e³
          ÀÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÙ
          31                                                             0
    
            where   m  - 24-bit mantissa
                    s  - sign of the number
                    e  - 7-bit exponent in excess 64 notation
    
    The mantissa is considered to be a binary fixed point fraction and except
    for zero it is always normalized (has a one bit in its highest position).
    Thus, it represents a value of less than one but greater than or equal to
    one-half.
    
    The sign bit is a zero for a positive value, and a one for a negative
    value.
    
    The exponent is the power of two needed to correctly position the mantissa
    to reflect the number's true arithmetic value. It is held in excess 64
    notation which means that the two's complement values are adjusted upward
    by 64, thus changing 40H (-64) through 3FH (+63) to 00H through 7FH. This
    facilitates comparisions among floating-point values.
    
    The value of zero is defined as all 32 bits being zeroes. The sign,
    exponent, and mantissa are entirely cleared. Thus, zeroes are always
    treated as positive.
    
    The range allowed by this format is as follows:
    
    DECIMAL                18                                 -20
            9.22337177 * 10    >  +VALUE    >  5.42101070 * 10
                           18                                 -20
           -9.22337177 * 10    >  -VALUE    > -2.71050535 * 10
    
    BINARY (HEXADECIMAL)
                        63                                   -63
           .FFFFFF  *  2       >  +VALUE    >   .FFFFFF  *  2
                        63                                   -63
          -.FFFFFF  *  2       >  -VALUE    >  -.FFFFFF  *  2

    SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 6
    

    3.3. Application Service
         -------------------

    For the exact definitions of the Instructions used by the PCD to use
    this service, please see the PCD Reference Manual.
    
    3.3.1. Variable Access Service
           -----------------------

    Each variable has a certain Type.  The following Types are defined for
    the PCD:
    
         ÚÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³  code: ³ type:                 ³ formats:                 ³
         ÃÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
         ³  R     ³ register              ³ integer / floating point ³
         ³  C     ³ counter               ³ positiv integer          ³
         ³  T     ³ timer                 ³ positiv integer          ³
         ³  F     ³ flag                  ³ binary                   ³
         ³  I     ³ input                 ³ binary                   ³
         ³  O     ³ output                ³ binary                   ³
         ³  K     ³ the real time clock   ³ special format           ³
         ³  D     ³ the display register  ³ any format               ³
         ÀÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
    On these variables the Read Service and the Write Service is defined,
    one may read or write these variables.  The variables are accessed by
    its logical nummeric address (direct addressing).
    
    3.3.2. Status Service
           --------------

    The status of the PCD may be requested by the Client.  The following
    states are defined for each Prozessor in the PCD:
    
            S       Stopped (by the debugger)
            H       Halted  (by different reasons)
            R       Running
            C       Conditional running (by the debugger, waiting for
                    breakpoints)
            D       Disconnected (this Prozessor is not in the PCD)
    

    SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 7
    

    3.4. Application Protocol
         --------------------

    Two different protocol procedures between a Client and a Server are used.
    
    <write-request>  -> does not ask any response
    <read-request>   -> asks a <read-response>
    
    Write & control procedure:
    -------------------------
    
    CLIENT                                            SERVER
       ³                                                ³
       ³-------------<write request>------------------->³ write or control
       ³                                                ³ action
    
    
    Read procedure:
    --------------
    CLIENT                                           SERVER
       ³                                                ³
       ³-------------<read request>-------------------->³ read action
       ³                                                ³
       ³                                                ³
       ³<------------<read response>--------------------³
       ³                                                ³
    
    3.5. Conformance Classes
         -------------------

    There are two classes of application services defined.
         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³  Class                 ³ included Services          ³
         ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
         ³  reduced P8 Protocol   ³ Variable Service           ³
         ³  MD/SD mode            ³ State Service              ³
         ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
         ³  full P8 Protocol      ³ Further telegrams          ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

    SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 8
    

    4. PRESENTATION LAYER
       ------------------

    The Presentation Layer ensures that the information is delivered to the
    communicating application process in a form that can be used and
    understood. While the meaning - semantics - of the information is fully
    preserved, the format and language difference - syntax - is defined.
    
    4.1. Syntax Representation
         ---------------------

    
        +- function and name
        |
        v
        read input, output, flag
     01 cmd ::=      'R' ('I' | 'O' | 'F') <count> <address-IOF>
        sts ::=      {<bit-value>}+
     ^  ^ ^
     |  | |
     |  | +--sts status telegram from the SERVER to the CLIENT
     |  |     the <read response> entity
     |  |
     |  +--cmd command telegram from the CLIENT to the SERVER
     |      the <request> entity
     |
     +---command code for the telegram (internal registration)
    
    
     { <a> }+  represents :
    
             - for read   (<count>+1) occurrences of the expression <a>
             - for write  ( 1 to 16 ) occurrences of the expression <a>
    
             - for read/write user memory
                          (<length+1>)  occurrences of the expression <a>
                                        length max. = 1F hex
    
     [ <a> ]   represents an optional parameter
    
    4.2. General Definitions
         -------------------

    
     <break-point>   ::= 'S' <status> <mask> |
                         'D' <operator> <8-hex-digit> |
                         'N' <operator> <4-hex-digit> |
                         ('I' | 'O' | 'F' ) <address-IOF> <bit-value>|
                         'P' <operator> <address-prog> |
                         'E' <op-code> |
                         ('R' | 'T' | 'C' ) <address-RTC> <operator>
                                                            <8-hex-digit> |
                         'B' <8-hex-digit>
                         'L' <op-code><operand>
    
     (arithmetic Status, Display register, Input, Output, Flag,instruction

    SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 9
    

      Pointer, op-codE, Register, Timer, Counter, numBer of steps,
      iNdex register, instruction Line)
    
     <count>         ::= <hex-digit>       ; value 0 means 1 count !
     <address-IOF>   ::= <4-hex-digit>
     <address-RTC>   ::= <3-hex-digit>
     <address-prog>  ::= <6-hex-digit>
     <address-68000> ::= <6-hex-digit>
     <op-code>       ::= <3-hex-digit>
     <operand>       ::= <4-hex-digit>
     <text-number>   ::= <3-hex-digit>
     <char-position> ::= <4-hex-digit>
     <number-of-chars> ::= <4-hex-digit>
     <bloc-type>     ::= <hex-digit>
     <bloc-number>   ::= <3-hex-digit>
     <ascii-char>    ::= <2-hex-digit>
     <length>        ::= <2-hex-digit>
     <fail-address>  ::= <8-hex-digit>
     <nbr_elements>  ::= <4-hex-digit>
     <2-hex-digit>   ::= <hex-digit> <hex-digit>
     <hex-digit>     ::= '0' | '1' | '2' | '3' | '4' | '5' | '6' | '7' |
                         '8' | '9' | 'A' | 'B' | 'C' | 'D' | 'E' | 'F'
    
     <fail-text>     ::= <16-character>
     <module-type>   ::= <5-character>
     <version>       ::= <3-character>
     <cpu-number>    ::= <character>
     <character>      := printing character code: 20hex -> 7Fhex
    
     <clock-value>   ::= <week-year> <day-week> <year> <month> <day> <hour>
                         <minute> <second>
     <fail-date>     ::= <year> <month> <day> <hour> <minute> <second>
     <week-year>     ::= <dec-digit> <dec-digit>
     <day-week>      ::= <dec-digit> <dec-digit>
     <year>          ::= <dec-digit> <dec-digit>
     <month>         ::= <dec-digit> <dec-digit>
     <day>           ::= <dec-digit> <dec-digit>
     <hour>          ::= <dec-digit> <dec-digit>
     <minute>        ::= <dec-digit> <dec-digit>
     <second>        ::= <dec-digit> <dec-digit>
     <dec-digit>     ::= '0' | '1' | '2' | '3' | '4' | '5' | '6' | '7' |
                         '8' | '9'
     <status>        ::= <flags>
     <mask>  º        ::= <flags>
     <flags>         ::= <zero-flag> <neg-flag> <error-flag> <accu-flag>
     <zero-flag>     ::= <bit-value>
     <neg-flag>      ::= <bit-value>
     <error-flag>    ::= <bit-value>
     <accu-flag>     ::= <bit-value>
     <bit-value>     ::= '0' | '1'
    
     <operator>      ::= '<' | '=' | '>' | '#'
                         '#' means  not equal
    
     <sblock>        ::= <2-hex-digit>
     <act_trans>     ::= <4-hex-digit>[<act_trans>]

    SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 10
    

    
    4.3. Reduced Protocol Telegrams
         --------------------------

    4.3.1. Read Telegrams
           --------------

        read input, output, fla
     00 cmd ::=      'R' ('I' | 'O' | 'F') <count> <address-IOF>
        sts ::=      {<bit-value>}+
    
        read register, timer, counter
     01 cmd  ::=     'R' ('R' | 'T' | 'C') <count> <address-RTC>
        sts  ::=     {<8-hex-digit>}+
    
        read real time clock
     07 cmd  ::=     'RK'
        sts  ::=     <clock-value>
    
        read display register
     10 cmd  ::=     'RD'
        sts  ::=     <8-hex-digit>
    
    4.3.2. Write Telegrams
           ---------------

        write output, flag
     20 cmd  ::=     'W' ('O' | 'F') <address-IOF> {<bit-value>}+
        sts  ::=     empty
    
        write register, timer, counter
     21 cmd  ::=     'W' ('R' | 'T' | 'C') <address-RTC> {<8-hex-digit>}+
        sts  ::=     empty
    
        write real time clock
     27 cmd  ::=     'WK' <clock-value>
        sts  ::=     empty
    
    4.3.3. Read Status Telegram
           --------------------

        read PCD status
     11 cmd  ::=     'RS' ( '0' | '1' | ... | '6' | '7' )
                             0->6 cpu number ;   7 own
        sts  ::=     'S' | 'H' | 'R' | 'C' | 'D'
    

    SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 11
    

    4.4. FURTHER TELEGRAMS
         -----------------

    The following telegrams CANNOT be accessed from MD/SD mode, however
    the SAIA LIBRARY routines allow access to them under the following
    conditions :-
        PCD4/PCD6.M540/PCD2 : The PGU port and the K111 cable are used.
        PCD6                : The P800 is used
    
    Definitions
    -----------
        <count>         1 hex digit: 0..F (0=1 item, F=16 items)
        <bloc-type>     2 hex digits: 07=DB
        <block-number>  4 hex digits (0000H..FFFFH)
        <db-number>     4 hex digits (0000H..1F3FH)
        <db-element>    4 hex digits (0000H..3FFFH)
    
    NOTES:
    1)  The existing <bloc-number> is only 3 hex digits (0..4095),
        the new <block-number> is 4 hex digits (0..65535).
    
    2)  The existing <text-number> is only 3 hex digits (0..4095),
        the new <txt-number> is 4 hex digits (0..65535).
    
    3)  The existing <bloc-type> has a value 7 for data blocks (DB).
    
    4)  When writing the firmware for the new data memory, take into
        account that the "type" indicator byte may be extended later,
        and may not always be 8 (text) or 32 (data block).
    
    5)  The read/write text and data block telegrams may attempt to
        access characters or elements beyond the end of the text/DB.
    
        For texts/DBs 0..3999, the length can only be determined by
        reading it all until the NUL terminator is found. This is
        slow, therefore NO checks should be done by the firmware to
        detect access beyond the end of a text/DB (this is how it is
        with the existing firmware). It is the responsibility of the
        application program (PG1/PG3) to determine the length first,
        using the "read block size" telegram.
    
        For texts/DBs 4000..7999, the length is known, therefore
        telegrams which would access beyond the end must return a
        NAK immediately.

    SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 12
    

    4.4.1.  Read data block
           ----------------

    Works for data blocks 0..3999 in text memory (stored in encoded
    binary format), and for data blocks 4000..7999 in the new data
    memory. Returns NAK if the DB doesn't exist or it's not a DB
    (0..3999: if 1st byte is not FFH, 4000..7999: if "type" is not
    32).
        cmd := 'RZ' <count> <db-number> <db-element>
        sts := {<8-hex-digit>}+
    
    
    4.4.2.  Write data block
           -----------------

    Works for data blocks 0..3999 in text memory (stored in encoded
    binray format), and for data blocks 4000..7999 in the new data
    memory. Returns NAK if the DB doesn't exist or is not a DB
    (0..3999: if 1st byte is not FFH, 4000..7999: if "type" is not 32).
    
        cmd := 'WZ' <db-number> <db-element> {<8-hex-digit>}+
    
    4.4.3.  Read block addresses
           ---------------------

    Returns the user-memory address of the start of a given block,
    text or data block, and up to 16 consecutive blocks. Returns
    <address-prog> = 0 if the block doesn't exist, or 0xFFFFFF if
    a text address is requested and the block is in use as a DB
    or vice-versa. Works for texts and data blocks in the existing
    text memory, as well as in the new data memory. The address is
    the long word offset from the start of user memory, min 100
    (NOT the start of the CPU's memory).
    
        cmd := 'R1' <count> <bloc-type> <block-number>
        sts := {<address-prog>}+
    
    
    4.4.4.  Read block sizes
           -----------------

    Returns the size of a one or more code blocks in program lines,
    texts in characters, or data blocks in elements.
    Returns a size of 0 if the item doesn't exist, or 0xFFFFFF if
    a text size is requested and the block is in use as a DB or
    vice-versa.
    
        cmd := 'R2' <count> <bloc-type> <block-number>
        sts := {<6-hex-digits>}+
    
        read system program version
     14 cmd  ::=     'RV'
        sts  ::=     <module-type> <version> <cpu-number>

    SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 13
    

    5. SESSION LAYER
       -------------

    5.1. Session Layer Service
         ---------------------

    The Session Layer provides the means for the cooperating systems to
    organize and synchronize their dialog and manage their data exchange.
    The session layer ensures that all information is received at the
    destination and does not get lost.
    
    The Session Layer provides for interaction management of the end to end
    communication, the management of whose turn it is to send is handled -
    simplex or half duplex.
    
    Through the use of a synchronisation procedure, the Session Layer can
    identify and recover from errors in the data flow.  It can also report
    to the application abnormal situations that have not been corrected.
    
    Two Session Layer Services are defined:
     - The controlled transmission of a message
     - The controlled invocation of a response message
    
    5.2. Session Layer Protocol
         ----------------------

    The Session Layer for the P8 - Protocol is based on DIN 66019.  This is
    an character oriented not transparent (code dependent) point to point
    protocol.  It may be used on synchronous or asynchronous transmissions.
    
    Note: DIN 66019 is normaly considered to be a Link Layer Protocol.
    However in this context it is used as an end-to-end protocol to control
    the dialog, what is exactly the Session Layer Function.
    
    5.2.1. Description of the used control-characters
           ------------------------------------------

    All characters use only 7 bits.  The transmitted telegrams from the
    presentation layer are not allowed to contain any of the following
    control characters.
    
    STX      Start of TeXt  (^B)
             A character delimiting that part of a message which
             constitutes the telegram.
      Note:  - is not included in the block checksum
    
    ETX      End of TeXt    (^C)
             A control character used to delimit the end of a series of
             characters constituting the telegram of a message.
      Note:  - requests a reply ACK or NAK
             - starts the timeout on the sender station
             - is followed of the block checksum
             - is included in the block checksum
    
    ENQ      ENQuiry   (^E)
             A communications control character used to solicit a response

    SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 14
    

             from another station. It is used as the request to send the
             values of the previous read request.
      Note:  - requests a NAK if the transmit buffer is empty
    
    ACK      ACKnowledgement  (^F)
             A control character which represents an affirmative response to
             a sender. It acknowledges error-free reception of a block or
             segment of a message.
      Note:  - cancels the timeout
             - frees the transmit buffer
    
    NAK      Negative AcKnowledge (^U)
             This character represents a negative response from the receiver
             to the sender. It indicates that a block of information has
ò             been received with errors and must be retransmitted.
    Note:  - the timeout is reset
             - the repeat counter is incremented
             - invokes a retransmission of the transmit buffer
    
    EOT      End of Transmission (^D)
             This control character is only used if the
             messagesynchronisation between the two partners is completely
             lost. It clears all buffers and counters and resets the initial
             state.
    
    BCC      Block Check Code (any value)
             The BCC is a seven bit code. It is the modulo 2 sum of all
             characters behind the STX character (excluding the STX
             character) and follows immediately the ETX character.
    
      Example:               STX
                             R       01010010
                             K       01001011
                             ETX     00000011
                                     --------
                             BCC     00011010
    

    SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 15
    

    5.2.2. Message transmission
           --------------------

    Each message is acknowledged by the receiving part.  The acknowledge
    means, that the corresponding action is already performed.  The sending
    part clears the transmission buffer only after the reception of the ACK
    and sends the next message.
    
    Sending                                           Receiving
       ³                                                ³
       ³----------STX<cmd>ETX BCC---------------------->³
       ³                                                ³ action
       ³<---------ACK-----------------------------------³
       ³                                                ³
       ³----------STX<cmd>ETX BCC---->   next message invokes next action
       ³
    
    On a transmission error the receiving part replies with a NAK and the
    sending part sends again the contens of the transmit buffer.  This
    mechanisme is repeated 3 times.  Afterwards the session layer informs
    the upper layers about the failure in the transmission connection.
    
    Sending                                           Receiving
       ³                                                ³
       ³----------STX<cmd>ETX BCC---------------------->³ BCC error
       ³                                                ³ detection
       ³<---------NAK-----------------------------------³
       ³                                                ³
       ³----------STX<cmd>ETX BCC---------------------->³ BCC correct
       ³                                                ³
       ³<---------ACK-----------------------------------³ action
       ³                                                ³
    
    If a message is not acknowledged after 3 seconds it is repeated. A
    message is repeated only 3 times.
    
       ³----------STX<cmd>ETX BCC------------>?????     ³
    3s ³                                                ³
       ³----------STX<cmd>ETX BCC---------------------->³
       ³                                                ³ action
    3s ³  ???<----ACK-----------------------------------³
       ³                                                ³
       ³----------STX<cmd>ETX BCC---------------------->³ repeat
       ³                                                ³ action
       ³<---------ACK-----------------------------------³
       ³                                                ³
    
    Note: The actions in the reduced SAIA-P8  protocol are defined that a
    way, that they can be repeated without any problems.
    

    SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 16
    

    5.2.3. Invocation of response messages
           -------------------------------

    A Server is not allowed to send any <read-response> telegrams to the
    Client without any prior enquiry (ENQ) command.  This mechansime allows
    the Client to prepare his internal receive buffer to receive the
    telegram.
    
    CLIENT                                           SERVER
       ³                                                ³
       ³----------STX<cmd>ETX BCC---------------------->³ action and
       ³                                                ³ preparation of
       ³<---------ACK-----------------------------------³ response (read
       ³                                                ³ value)
       ³                                                ³
       ³----------ENQ---------------------------------->³
       ³                                                ³ just creat the
       ³<---------STX<sts>ETX BCC-----------------------³ response and send
       ³                                                ³ it.
       ³----------ACK---------------------------------->³ clears the
       ³                                                ³ transmitbuffer
    
    Remark:  A NAK reply to the <read-response> just repeats the
    transmission of the transmit buffer contens.  The repetition of the ENQ
    creats anothertime the response message.  However on a <read-request> to
    read a variable, the value of the variable is only read on the action
    befor the ACK is returned.
    
    5.2.4. Simplex and Half-Duplex Protocol
           --------------------------------

    If both stations are Client and Server in the same time a half duplex
    protocol is used.  In the half duplex operation ENQ, ACK or NAK characters
    may be inserted in a datagram in the other direction.  The two stations
    must be able to detect these characters inside the messages.  A second
    message is only sended, if the previous message is acknowledged with ACK
    or the timeout of 3 seconds is reached.  To avoid deadlock conditions, one
    station in a half duplex configuration (both stations Client and Server)
    is the Master and the otherone the Slave.  In case of conflict, the
    Master-Client has priority over the Slave-Client.
    
    In a simplex operation one station is the Client and the otherone the
    Server.  As the transmitbuffer of the Server is only used for
    <read-response>, the Client does not need to acknowledge the
    <read-response>, it just passes the next request.
    
    To get full upward compatibility from the simplex to the half duplex
    operation, the <read-response> message is never repeated after a timeout
    by a Server.  The Client is free to ask a repetition of a wrong received
    <read-response> with a NAK within 3 seconds (retransmits the contens of
    the transmit buffer) or ENQ after 3 seconds (retransmits the response to
    the last request).
    

    SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 17
    

    5.3. Conformance Classes
         -------------------

    The Station with Client and Server must implement the half duplex
    Session Protocol and stations with only Server or only Client may
    implement the more simpler simplex protocol.

    SAIA - P8  REDUCED PROTOCOL DESCRIPTION                       Page: 18
    

    6. TRANSMISSION PROTOCOLS
       ----------------------

    6.1. Point to Point connection
         -------------------------

    The asynchronous connection has the following parameters:
    
     - speed in bit per second (bps)
     - number of bits per character ( 6,7 or 8)
     - parity Even / Odd / fix High / fix Low / No parity
     - number of stop bits (one or two)
    
    Example:
      short form:  9600,7,E,1
      meaning   :  speed 9600 bps , 7 bits/character, Even parity,
                   one stop bit
    
    See the PCD hardware manuals for the pin assignement and data of the
    communication interfaces.
    
    Note: There exist an additional protocol on the control lines for the PGU
    ----  class of interface.
    
      RTS   Request to send
    This signal is sended by the Client to ask the Server if he is ready to
    receive a message.
    
      CTS   Ready to sending
    This signal is used by the Server to reply to the RTS that it is ready to
    receive a message.
    
    Telegrams received without correct control lines on the PGU class are
    refused with NAK.